## Slide 1: 高通私有代码编译及打包

## Slide 2: Boot Loaders
cd boot_images/QcomPkg/Msm8998Pkg
Build images –
python ../buildit.py --variant LA -r RELEASE -t Msm8998Pkg,QcomToolsPkg
Clean the Build –
python ../buildit.py --variant LA -r RELEASE -t Msm8998Pkg,QcomToolsPkg --build_flags=cleanall

## Slide 3: MPSS
cd modem_proc/build/ms
source setenv.py
Build images
./build_variant.py 8998.gennm.prod bparams=-k
Clean the Build –
./build_variant.py 8998.gennm.prod --clean

## Slide 4: TrustZone
cd trustzone_images/build/ms
Build images –
python build_all.py -b TZ.BF.4.0 CHIPSET=msm8998 --recompile
Clean the build –
python build_all.py -b TZ.BF.4.0 CHIPSET=msm8998 –c

## Slide 5: ADSP
cd adsp_proc/build
Build images
python build.py -c msm8998 -o all
Clean the build
python build.py -c msm8998 -o clean

## Slide 6: RPM
Windows环境编译
Build images –
build_8998.bat
Clean the Build –
build_8998.bat –c

## Slide 7: SLPI
cd slpi_proc/build/
Build images
python ./build_v1_v2.py
Clean the build
rm –rf obj_v1 obj_v2
python ./build.py –c msm8998 –o clean

## Slide 8: 拷贝Android部分编译产物
拷贝Android部分编译产物：
至 私有代码：

## Slide 9: 打包
私有代码根目录下
./pack_apq8098.sh

## Slide 10: Provision
DUT 进入QFIL烧录模式
QFIL 设置
1. Configuration, click Provision ->OK
2. Select Build, Browser: /common/config/ufs/provision/provision_toshiba.xml
3. Select Programmer: /boot_images/QcomPkg/Msm8998Pkg/Bin/8998/LA/RELEASE/prog_ufs_firehose_8998_ddr.elf
4. Click Provision
5. USB Download 短接，重新进入 QFIL 烧录模式

## Slide 11: 烧录
DUT处于QFIL烧录模式
QFIL 设置
1. Configuration，Device Type->UFS, Reset/Erase
2. Build Type -> Meta Build
3. Select Build: /contents.xml
4. Download Content

## Slide 12: EVT 修改
Sensor GPIO
/vendor/qcom/proprietary/sensors/dsps/reg_defaults/sensor_def_qcomdev.conf
Camera
/kernel/msm-4.4/arch/arm64/boot/dts/qcom/msm8998-camera-sensor-cdp.dtsi
Fastmmi
1.读取默认WIFI MAC地址 2.读取默认SN 3.默认不支持充电，需要AP Utility
FFBM关机
/vendor/qcom/proprietary/fastmmi/mmi/input.cpp
Sensor rollback (private code)
boot_images/QcomPkg/Library/PmicLib/target/msm8998_pm8998_pmi8998/system/src/pm_sbl_boot_oem.c
rpm_proc/core/pmic/pm/config/msm8998/pm_config_target.c

## Slide 13: IMU Calibration
[Sensor] modify acc calibrate and Y axis data > 0.1
vendor/qcom/proprietary/sensors/dsps/reg_defaults/sensor_def_qcomdev.conf
vendor sensor gyro calibrate commit:9cdb25f3b5e08500166790ecb42d8f3e15506cfc
vendor/qcom/proprietary/sensors/dsps/test/src/sns_cm_test.cpp